## Slide 1
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 2
Variation of light intensity
Measuring the light intensity of different light sources
Objective
Relate light intensity and light source efficiency to create a hypothesis about the amount of light sent out by different light sources and proceed it to test using the Labdisc light sensor.

## Slide 3
The aim of the introduction is to focus students on the lesson subject by refreshing acquired knowledge and asking questions which encourage research development. Key concepts from the theoretical framework, applied by the students during the lesson, are taught.
Introduction and theory
Introduction
Have you ever experienced a electricity blackout when it is dark outside? Usually people run to find candles and flashlights so they can see something in the pitch-black. Even if we try to light the room by placing several candles around, or use the most powerful flashlight we have, it may still not be enough to brighten the room as well as a light bulb could.
Variation of light intensity
Measuring the light intensity of different light sources
How should we place several candles in a room in order to achieve the most light?

## Slide 4
Introduction and theory
What do you think the efficiency of a light source depends on?
Carry out the experiment activity with your class so that at the end you’ll be able to answer the following question:
How are the intensity and efficiency of a light source related?
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 5
Theoretical
The luminous flux gives us an idea about the light intensity sent out by light sources in all space dimensions, for example by a light bulb. But when you consider a projector, it is clear that it lights only in one direction - forward. That is why we need to know how the luminous flux is distributed into every space dimension, using the definition of light intensity.
Introduction and theory
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 6
Introduction and theory
Light intensity (I) is defined as the “luminous flux that is emitted per unit of solid angle (steradian) into a specific direction”. The unit of measure is the lumen per steradian, or candela (cd).
The mathematical equation that defines light intensity is:
Variation of light intensity
Measuring the light intensity of different light sources
What is this?
• = light intensity (cd)
• F = luminous flux (it is measured in lumens, meaning luminous power perceived per unit area)
• = differential of solid angle (steradians)

## Slide 7
Introduction and theory
Now students are encouraged to raise a hypothesis which must be tested with
an experiment.
If light intensity and light efficiency are related, how would the efficiency vary depending on the light source?
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 8
Activity description
Students will measure the light intensity of different light sources using the Labdisc light sensor. Based on the results, the students will proceed to relate each light source to its corresponding light efficiency.
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 9
Labdisc
Resources and materials
USB connector cable
LED flashlight with batteries
Candle
Lamp with an 11 watt vial
Matches
Fluorescent light bulb
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 10
Using the Labdisc
a. Using the Labdisc
Variation of light intensity
Measuring the light intensity of different light sources
To collect measurements with the Labdisc light sensor, the Labdisc must be configured according to the following steps:
Turn on the Labdisc by pressing
Press , and select “SETUP” by pressing
Now select the option “SET SENSORS” with
Select only the light sensor and then press
Once you have done that, you will return to setup, press once and
select “SAMPLING RATE” with
Select “MANUAL” with and then press

## Slide 11
Using the Labdisc
Variation of light intensity
Measuring the light intensity of different light sources
Press and select “NUMBER OF SAMPLES” with
Select “MANUAL” with and then press
To return to the measurements press three times.
Then press to start measuring.
Press the button each time you want to measure.
Once you`ve finished measuring stop the Labdisc by pressing
(you will see the instruction “Press SCROLL key to STOP”) and press

## Slide 12
Experiment
The following steps explain how to perform the experiment:
Place the four different light sources approximately 30 cm. away, in the following order: Lamp, flashlight, fluorescent bulb and candle. Darken the room covering the windows and turning off any artificial light sources.
To collect the data place the sensor approximately 10 cm. away from the light source.
Push the button of the Labdisc.
Turn the lamp on and observe how the measurements vary on the Labdisc screen.
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 13
Experiment
Wait until the intensity value you are measuring stabilizes.
Variation of light intensity
Measuring the light intensity of different light sources
Take just one manual sample of the light intensity.
Once you are done with the lamp - turn it off without turning off the Labdisc, and then turn on the LED flashlight. Repeat step five and six.
Measure the light intensity of the candle and the fluorescent tube as you did with the other light sources.
Leave the dark room in order to measure the light intensity in the outdoor sunlight and then the intensity of light when pointing the light sensor directly at the sun.
Once you`ve finished measuring turn the Labdisc off.

## Slide 14
Results and analysis
The following steps explain how to analyze the experiment results:
Variation of light intensity
Measuring the light intensity of different light sources
Connect the Labdisc to the computer using the USB communication cable or via the Bluetooth wireless communication channel.
On the upper menu press the button and select
Select the last experiment of the list.
Observe the graph displayed on the screen.
Press the Bar-graph icon and set the display to a Bar Graph display.
Press the button and write annotations on the graph specifying your observations according to the moment you registered the data.

## Slide 15
Results and analysis
How do the data curves vary for each light source?
How do the results relate to your initial hypothesis? Explain.
What similarities do the data curves present?
Variation of light intensity
Measuring the light intensity of different light sources
Which was the brightest light source? Which was the least bright?

## Slide 16
Results and analysis
The graph below should be similar to the one the students came up with.
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 17
Conclusions
What was the variation between the different light sources you analyzed?
Students should analyze the different values of light intensity, defining which were
the highest and lowest and the range of variation between them.
Following are some questions and answers which should be developed by students in order to elaborate on their conclusions.
How does the amount of light relate to the light intensity?
Students should relate more powerful light sources to greater light intensity and less bright light sources, like a candle, to less light intensity.
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 18
Conclusions
Variation of light intensity
Measuring the light intensity of different light sources
How do you think the light flux varies in each of the light sources you analyzed?
Students should conclude that the more light intensity, the more luminous flux there is. Both
parameters depend on the relative distance between the location of the Labdisc light sensor and
the light source.
According to your experience, which do you think is the most efficient light source
from the three artificial sources studied?
Students should indicate that the most efficient light source is the LED flashlight,
because it uses less energy to function, for this reason it is considered to be energy saving.
Students should reach the following conclusions:
Different light sources have different light intensities and this relates to their associated functions. However, light intensity cannot be related to the efficiency of the source. The LED flashlight is not the most luminous source, but presents greater energy efficiency than the candle and the lamp. On the other hand, sunlight is the most powerful light source and yet, is the most efficient.

## Slide 19
Activities for further application
How could you increase the light intensity of a candle?
Students should explain that they could achieve this by increasing the amount of
light the candle produces, in other words, making the flame larger. We can establish the following connection: The larger the candle flame is, the more light intensity it produces, and vice versa (the smaller the candle flame, the less light intensity).
The aim of this section is for students to extrapolate the acquired knowledge during this class through its application in different contexts and situations. Furthermore, it is intended that students question and present possible explanations to the experimentally observed phenomena.
Further questions:
Variation of light intensity
Measuring the light intensity of different light sources

## Slide 20
Activities for further application
How are light intensity and electric power related?
Students are expected to establish that light sources which emit more light intensity use more energy in the process. On the other hand, we should point out the example of the candle, which uses less energy in the lighting process. In both cases energy is “lost” through heat. This shows that light efficiency depends on how much energy we use to illuminate, rather than produce heat.
Variation of light intensity
Measuring the light intensity of different light sources
How is a natural light source like the sun different from an artificial light source such as a light bulb?
Students should quantify that the sun’s light intensity is much higher than the intensity of any artificial light source, and that this depends directly on the amount of energy used by the sun to produce this intensity of light.